## Slide 1: CS-E5360 Systems of Systems Practical Session
Asad Javed
PhD Researcher
Computer Science
Avleen Malhi
Postdoctoral Researcher
Computer Science
Notes: 10 s.

## Slide 2: Agenda
Introduction
O-MI/O-DF Reference Implementation
How to run O-MI node
Live demos
(Scripts and Slides are available at: https://github.com/AaltoAsia/SoS-Scripts)

## Slide 3: Introduction
This session will address the practical aspects of using IoT technology to deliver smart city solutions.
Goal of the session:
  Install O-MI Node reference implementation
  Use an IoT device to send sensor values to your Node
  Make a data subscription to send value from your Node to our Node
We will have live visualization of all the data coming to our O-MI Node

## Slide 4: O-MI/O-DF Reference Implementation
Open source implementation developed at Aalto University
  Available at: https://github.com/AaltoAsia/O-MI
Enable fast deployment of IoT node

## Slide 5: How to run O-MI node?
Dependency Java JDK 1.8
Run pre-compiled node:
  Download the latest release version and unpack it. Available at: https://github.com/AaltoAsia/O-MI/releases
    For Windows: Use “o-mi-node-1.0.9.zip” (Don’t use deep directory structure)
    For MAC/Linux: Use “o-mi-node-1.0.9.tgz”
  To allow write requests from other machines you need to modify file “<Extracted folder>/conf/application.conf”.
    Change the setting “allowRequestTypesForAll”, add “write” to the list, such that the result looks like this:
    allowRequestTypesForAll = ["read", "cancel", "call", "write"]
  For Windows: Go to the <Extracted folder>/bin and click on o-mi-node.bat For MAC/Linux: cd <Extracted folder>/bin and run “./ o-mi-node”
  The server can now be accessed with URL http://localhost:8080/

## Slide 6: Open Firewall port for O-MI in Windows
Navigate to Control Panel -> System and Security -> Windows Firewall
Select ‘Advanced settings’ from the left menu and highlight Inbound Rules in the left pane
Right click Inbound Rules and select New Rule
Select ‘Port’ and click Next
Add the port you need to open and click Next
Select TCP protocol and add ’8080’ in the port field and click Next
Select Allow the connection in the next window and hit Next
Select the network type and click Next
Name the rule something meaningful and click Finish

## Slide 7: Case Study: Smart Home
O-MI/O-DF Web Client
Wrapper
Data Publisher
O-MI/O-DF Reference
Implementation
Data Analytics
Agent Manager 1
Agent 1
O-MI/O-DF Node Server
Agent 2
O-MI
Write
Request
O-MI
Subscription
O-MI
Response
Monitoring Unit

## Slide 8: Smart Home Scenario Description
Smart Home equipped with
  Temperature and Humidity sensor (SHT-20)
  CO2 sensor (S-100)
Wrapper to publish smart home data to O-MI node
  Read sensor value
  Translate it to O-DF
  Put it in O-MI Write request
  Send with HTTP POST request
Developer can test the system using web-client
Data consumer (Monitoring unit) might be interested in these sensor values for analyzing the required object values. It can subscribe to the objects of interest

## Slide 9: Hardware and Sensors Provided
ESP8266 WiFi development modules
SHT20 Temperature and humidity sensor
S-100 CO2 sensor

## Slide 10: Live Demo
Implementation Using ESP8266

## Slide 11: Download Scripts
Connect to our WiFi “TP-LINK_C5E618”
Open new termial and download the provided scripts from https://github.com/AaltoAsia/SoS-Scripts

## Slide 12: ESP8266 Arduino Configuration
The ESP8266 is a very low-cost Wi-Fi microchip with full TCP/IP stack and microcontroller capability.
Arduino is an open-source electronics platform based on easy-to-use hardware and software.
  Install latest Arduino IDE from https://www.arduino.cc/en/main/software
  Start Arduino and open Preferences window.
  Enter https://arduino.esp8266.com/stable/package_esp8266com_index.json into Additional Board Manager URLs field.
  Open Boards Manager from Tools > Board menu and install esp8266 platform
  For MAC machine, download and install the driver ”CH34x_Install_V1.5.pkg” from https://github.com/adrianmihalko/ch340g-ch34g-ch34x-mac-os-x-driver
  Restart the Arduino IDE

## Slide 13: CO2 Sensor (Model: S-100)
5V
GND
TX
Connect jumper cables:
  Sensor TX -> ESP RX
  Sensor GND -> ESP GND
  Sensor 5V -> ESP 5V

## Slide 14: Interfacing CO2 Sensor with ESP8266
Connect ESP chip with your laptop USB port.
Start Arduino IDE and select the following board from Tools -> Board
  LOLIN (WEMOS) D1 R2 and Mini
Select port using Tools -> Port
cd <....>/SoS-Scripts/CO2_test (for opening test scripts for CO2 sensor)
Open create_odf tab in Arduino and change <id> of the Object to something unique and change the url to your O-MI Node (http://yourIP:8080/)
Note: Disconnect the RX of ESP8266 while uploading the code.
Press Upload button
Connect RX of ESP8266 again after uploading is done.
If it fails you might have wrong port or too high upload speed
View the output through Tools -> Serial Monitor
  Select baud rate as 38400

## Slide 15: Temperature and Humidity Sensor (Model: SHT-20)
# ? * ?
+ GND * ?
*? * 3v3
*? * SDC
*? * SDA
GND
3.3V
SDC
SDA
Connect jumper cables:
  Sensor SDA -> ESP SDA (D2)
  Sensor SDC -> ESP SDL (D1)
  Sensor GND -> ESP GND
  Sensor 3.3V -> ESP 3V3

## Slide 16: SHT20 Sensor
Download the library for SHT20 from https://github.com/DFRobot/DFRobot_SHT20 into the ’libraries’ folder of your Arduino installation directory (<....>/Documents/Arduino/libraries).
cd <....>/SoS-Scripts/temp_humi_test (go to our scripts directory)
Open create_odf tab in Arduino and change <id> of the Object to something unique and change the url to your O-MI Node (http://yourIP:8080/)
Press Upload button
Tools -> Serial Monitor
  Select baud rate as 115200

## Slide 17: Create a subscription for our visualization Node
Go to http://localhost:8080/ and go to ”O-MI Test Client WebApp”
Check that your data have been received correctly with a Read request, after that, continue with subscription:
Select ”Objects” from the O-DF tree
Select ”Subscription” request
Open ”Optional parameters”
Put address of the visualization node (http://192.168.1.20:8080/) to ”callback” field
Press ”Send” and see if your value shows on the visualization (after it changes next time)

## Slide 18
Questions